## Slide 2: Corporate Wide Area Networks (WANs)
Chapter 10

## Slide 3: 10.1: LANs versus WANs (and MANs)
Category | Local Area Network | Wide Area Network
Abbreviation | LAN | WAN
Service Area | On customer premises (home, apartment, office, building, campus, etc.) | Between sites in a region, a country, or around the world.
Implementation | Self. | Carrier.
Cost per bit | Low | High.
Typical speed | Gigabits per second | 1 to 100 Mbps typical

## Slide 4: Corporate WANs
The Internet
  Ubiquitous and inexpensive
  Lacks the QoS requirements of organizations
Corporate WANs
  For transmission between a corporation’s sites
  Offer the required QoS
  Offer manageability
  Much more expensive than the Internet to meet traffic engineering requirements
2

## Slide 5: 10.4: The Public Switched Telephone Network (PSTN)
Residential Access

## Slide 6: 10.5: Asymmetric Digital Subscriber Line (DSL) Service for Residences

## Slide 7: 10.6: Cable Modem Service
1
8
7
6
5
4
3
2

## Slide 8: 10.7: Coaxial Cable
Two conductors: central wire and coaxial ring

## Slide 9: ADSL versus Cable Modem Service
In general …
  Cable modem service offers somewhat faster individual throughput at a somewhat higher cost.
  ADSL service offers somewhat slower individual throughput at a somewhat lower cost.
  Both types of carrier and new entrants are bringing fiber to the home for far faster speeds

## Slide 10: 10.8: Cellular Telephone Service
Note that a cell is a geographical region while a cellsite is a building with cellular equipment

## Slide 11: 10.9: Cellsite for Mobile Telephones
Cellsite
Cellular
Antennas
Point-to-Point Microwave
Antenna to MTSO

## Slide 12: 10.8: Cellular Telephone Service
4.
A channel can be reused in multiple cells.
The carrier can serve more customers.

## Slide 13: Cellular Technology
Channel Reuse
  Example without channel reuse:
    If 500 channels, only 500 simultaneous subscribers can be served in the entire system.
  Example with channel reuse in each cell
    500 channels
    100 cells
    Can serve 50,000 simultaneous subscribers

## Slide 14: 10.8: Cellular Technology
If you travel between cells, you will be handed off to a new cell site in the new cell (P)

## Slide 15: 10.10: Cellular Data Speeds
Speeds
  Early cellular systems were limited to about 20 kbps
  Today, most carriers give peak download speeds of 5 to 10 Mbps with the best giving 15 to 20 Mbps
  100 Mbps is on the horizon
  Nearly all carriers now use LTE (long-term evolution) technology

## Slide 16: 10.10: Cellular Data Speeds
LTE Advanced
  The next generation of LTE
  Currently, speeds are required to be 3 Gbps downstream, half of that upstream
3G, 4G, and 5G
  The ITU creates definitions of generations
  Marketers are using the terms in a meaningless manner

## Slide 17: 10.10: Cellular Data Speeds
Throughput Differs Widely from Rated Speeds
  If the user is riding in a car, throughput will fall.
  If more customers use a cellsite, the cellsite must decrease the transmission speed to each.
  In particular, changing numbers of users means that speed will depend on the time of day.
Copyright © 2015 Pearson Education, Inc.

## Slide 18: 10.12: Access Lines vs Leased Lines
Each customer site must have a CSU/DSU interface to the telephone network.
Corporate
Site
Corporate
Site or Carrier Point of Presence (POP)
Trunk
Link
Trunk
Link
Corporate
WANs

## Slide 19: 10.13: Leased Line Data Network
There are many types of leased lines with different speeds (and prices)

## Slide 20: 10.13: Leased Line Data Network
Company must plan, install, and operate its own leased line network

## Slide 21: 10.18 MPLS Networks
MPLS Carrier provides a business WAN service
  Carrier does all of the management work
Customers only need leased lines to MPLS Carrier POPs
  Points of Presence
  Access points to the MPLS network
Company
Carrier MPLS Network
Leased Line
POP

## Slide 22: 10.18: Multiprotocol Label Switching (MPLS)

## Slide 23: 10.18: Multiprotocol Label Switching (MPLS)
Router 3 sends the packet out through Interface 1
Each label-switched path is given a label number, which is placed before each packet.

## Slide 24: 10.18: Multiprotocol Label Switching (MPLS)
However managing traffic engineering is expensive, so MPLS costs more than using the Internet

## Slide 25: Using the Internet for Corporate WAN Transmission
Advantages Compared to MPLS
  Inexpensive per bit transmitted compared to MPLS
  Reaches Everywhere
Disadvantages Compared to MPLS
  No security
  No SLAs
  No ability to manage in detail
New: Not in Book

## Slide 26: Hybrid WANs
Concept
  Use the Internet for traffic that allows it
  Use MPLS for traffic that needs it
Implementation
  Far easier said than done
  Requires network management software that can implement it
New: Not in Book

## Slide 27: Mixing and Matching
In general, must use multiple carriers and services
  Leased lines between sites are often the only alternatives
  MPLS carriers may be regional
    May have to deal with several
    Interoperability is often limited
  Use the Internet where you can
  Corporate WANs are a patchwork
New: Not in Book

## Slide 28: All Pau